***   UTILITIES NOTES   ***


[A] -- WTS30.EXE --
    ===============
    It is a utility for helping user to select Where To Show the
    output. User can change the display output to LCD / CRT or LCD & CRT
    simultaneously.


[B] For IDE Local BUS ....

    -- IDEINS.BAT --
    ================
    IT is a utility for helping user to install the IDE Local BUS
    Driver for MicroSoft WINDOWS 3.x .
    TO install s1000.386 to a window directory C:\WINDOWS type:

           ideins c:\windows


    -- ADDDRV.EXE --
    ================
    It will make a copy of WINDOWS's SYSTEM.INI named SYSTEM.100.
    In which file, the S1000.386 be installed.

    ps.  : It be used in IDEINS.BAT

    -- DEVA05S.SYS --
    ================
    DEVA05S.SYS is used to set speed and multi-sector numbers
    for both 1st and 2nd IDE channels (for 2nd channel only
    speed setting).

    It also makes 1st channel multi-sector transfer active to
    increase the HDD performance.

    To use it, the following command should be append to your
    CONFIG.SYS file.
          device=[drive]:\[path]\DEVA05S.SYS [1st speed]
                 [1st multi-sector] [2nd speed]

    After reset your system, DEVA05S.SYS will take effect.

    If you do not specify speed settings, DEVA05S.SYS will
    ask you to fill it.

    If you do not specify multi-sector numbers, DEVA05S.SYS
     will use default number (20H).

[C] For CD-ROM Driver ....
    If you wont to install a CD-ROM, there are some things to do
       1. set the CD-ROM I/O port to 230h
       2. set LastDrive=Z
       3. add the following command to AUTOEXEC.BAT
          c:\dos\MSCDEX.EXE /D:MSCD001 /V /L:H
                                         ^^^^^^set CD-ROM as H: Drive

    Ex.  For a MITSUMI Double Speed CD-ROM, The following two line
       have to be added to CONFIG.SYS :

         device=c:\utl\MTMCDAS.SYS /D:MSCD001 /V/C /P:230
         LastDrive=Z                              ^^^^^^^^


 [D] For MOUSE Driver

     MOUSE.COM       Mouse driver as a command (call from AUTOEXEC.BAT
                     or DOS prompt)
     MOUSE.SYS       Mouse driver as a device driver ( call from
                     CONFIG.SYS )

     MTUTOR.EXE      Work file for mouse tutorial
     MTUTOR.SCR

     GTEST.EXE       Work file for mouse test